Adobe Illustrator print to laser instructions;

- Artboard size 18” x 32” or less. If oversized; Document Setup > Edit Artboards > 18” h. 32” w. Artboard must be landscape oriented if over 18” x 18”

- File > Document Color Mode > RGB

- Select All > Stroke - .01

- Select color, check saturation 255.

- If necessary Select color > Select > Same > Stroke Color >                          check saturation at 255, 0, 0. Work through all colors. Black is 0, 0, 0.

- If any color fills are unintentionally present Select All > No Fill

- File > Print, Custom to VersaLaser, Print.

- Open laser interface, analyze drawing. If ok.

- Settings > Load > Select material, open > OK

- Start laser, Start exhaust, Press play.

AutoCAD print to laser;

- Select All > Lineweight to 0.00

- File > Print

- Plotter to VLS 6.60

- Paper size user defined landscape

- Plot area > window > pick window

- Scale; fit to paper, 1 to 1, or other

- OK, or Preview > Plot

- Open laser interface, analyze drawing. If ok.

- Settings > Load > Select material, open > OK

- Start laser, Start exhaust, Press play.

RhinoCAD print to laser;

- Select All > Properties > Print Width > .01 > enter.

- File > Print

- Destination VLS 6.60

- Printer output > Vector output

- Output Color > Display Color

- View > Window or other

- Scale > 1 to 1 or other

- Print

- Open laser interface, analyze drawing. If ok.

- Settings > Load > Select material, open > OK

- Start laser, Start exhaust, Press play.